## Slide 1
SignSpeak AI
See It • Understand It • Recognize It
AI-Powered Real-Time Hand Gesture Recognition with Handwriting-to-Text Write Mode
Bhavya Maheshwari
Mody University of Science and Technology

## Slide 2
SignSpeak AI
2
The Communication Gap
Why gesture and handwriting recognition still fall short
Interpreter Dependence
Gesture-based communication often still needs a human interpreter in the loop.
Fragmented Tools
Gesture recognition and handwriting recognition usually live in separate, disconnected apps.
Rigid Systems
Many existing solutions are rule-based and static, not adaptive to a real, moving hand.

## Slide 3
SignSpeak AI
3
What is SignSpeak AI?
SignSpeak AI is a real-time hand gesture recognition system built with computer vision and machine learning.
It tracks 21 hand landmarks live from a webcam, classifies the gesture with a trained Random Forest model, and layers a second mode on top: a handwriting canvas that turns mouse-drawn letters into text using OCR.
One application, two ways to communicate.
Real-time recognition
Live gesture classification, smoothed over recent frames
Gesture Mode
Camera-based hand landmark detection with MediaPipe
Write Mode
Draw letters, get text, build a sentence — powered by OCR

## Slide 4
SignSpeak AI
4
Technology Stack
Python
Core language
OpenCV
Video capture & drawing
MediaPipe
Hand landmark detection
Scikit-Learn
Random Forest classifier
Pandas / NumPy
Dataset handling
Tesseract OCR
Handwriting recognition

## Slide 5
SignSpeak AI
5
How It Works — Live Pipeline
1
Camera Feed
Webcam captures live video
2
Landmark Detection
MediaPipe extracts 21 hand points
3
Normalization
Wrist-relative + scale-invariant features
4
ML Classification
Random Forest predicts the gesture
5
Gesture Output
Smoothed label shown on screen

## Slide 6
SignSpeak AI
6
Feature — Gesture Mode
Live camera feed with a real-time bounding box around the detected hand
21-point hand landmark tracking via MediaPipe
Wrist-relative + scale-normalized features — works at any distance from the camera
Majority-vote smoothing across the last 8 frames for a stable label
Confidence threshold filters out low-confidence guesses ("Uncertain...")
Gesture : Palm Open

## Slide 7
SignSpeak AI
7
Feature — Write Mode
Draw letters or words freehand with the mouse on a white canvas
Choose from 4 pen colors plus an eraser, with full undo support
Tesseract OCR recognizes each word the moment you press "Add Word"
Recognized words build up into a running sentence
Every action works from on-screen buttons or keyboard shortcuts

## Slide 8
SignSpeak AI
8
Training the Gesture Model
A repeatable 4-step pipeline, run once per new gesture set
Collect Data
Record labeled landmark samples per gesture from webcam
Clean Dataset
Drop malformed or non-numeric rows before training
Train Model
Random Forest learns from normalized landmark features
Evaluate & Save
Accuracy + cross-validation, then save model & encoder

## Slide 9
SignSpeak AI
9
Engineering Highlights
Robustness fixes that make the app work reliably across machines
Portable Paths
File-location-based paths — works whether run from root or src/
Auto-Detected OCR
Finds Tesseract automatically instead of a hardcoded path
Scale-Invariant Features
Recognition stays accurate at any distance from the camera
Reliable Camera Access
DirectShow backend with warm-up retries on Windows

## Slide 10
SignSpeak AI
10
Future Scope
More Sign Language Gestures
Expand vocabulary toward ISL / ASL coverage
Text-to-Speech Output
Speak recognized gestures and sentences aloud
Mobile Application
Bring gesture and write recognition to phones
Deep Learning Upgrade
Move from Random Forest to a neural model for scale

## Slide 11
Thank You
SignSpeak AI — See It, Understand It, Recognize It
github.com/bhavyamah23/SignSpeakAI
Bhavya Maheshwari
Mody University of Science and Technology